## Slide 1
Subsea Oil Pipeline Insulation Performance under High Thermal Stress
Mini Project 6 · Heat and Mass Transfer Lab (BMEE402P)
School of Mechanical Engineering (SMEC), VIT Vellore
Project Guide: Yagna S Mukkamala
Ishaan Pitambare (24BME0029)
Ojas Raverkar (24BME0046)
Arnav Deogaonkar (24BMV0087)

## Slide 2: Problem Definition and Novelty
1
Why it matters
Crude oil carries paraffin waxes. As the oil cools, wax solubility falls and crystals deposit on the pipe wall, progressively blocking flow (waxing).
2
What we studied
Thermal resistance and conductivity of insulation layers under rising thermal load, then 10 km of multilayer subsea pipe, to keep oil above 45 °C.
3
Novelty
Textbooks treat k as constant. We tested whether real layer resistance holds, degrades or rises with load, for flow assurance and insulation design.

## Slide 3: Data Acquisition: Interface Temperatures (°C)
Insulation | Oil inlet | Inner wall | Steel / insulation | Insulation / jacket | Jacket / concrete | Concrete / fouling | Outer surface | Seawater
Aerogel | 110 | 109.37 | 109.34 | 6.053 | 5.475 | 4.14 | 4.088 | 4
 | 50 | 49.727 | 49.715 | 4.933 | 4.598 | 4.061 | 4.038 | 4
Solid PP | 110 | 105.75 | 105.57 | 18.512 | 13.312 | 4.956 | 4.521 | 4
 | 50 | 48.155 | 48.077 | 10.297 | 8.0408 | 4.415 | 4.226 | 4
Syntactic PP | 110 | 106.66 | 106.52 | 15.393 | 11.31 | 4.751 | 4.409 | 4
 | 50 | 48.552 | 48.49 | 8.944 | 7.172 | 4.326 | 4.177 | 4
Advanced Syntactic Foam | 110 | 107.25 | 107.14 | 13.377 | 10 | 4.618 | 4.337 | 4
 | 50 | 48.808 | 48.757 | 8.069 | 6.611 | 4.2683 | 4.1463 | 4
Rigid PU Foam | 110 | 109.25 | 109.22 | 6.45 | 5.646 | 4.169 | 4.092 | 4
 | 50 | 49.674 | 49.66 | 5.113 | 4.714 | 4.073 | 4.04 | 4
Wood | 110 | 106.66 | 106.52 | 15.353 | 11.31 | 4.751 | 4.409 | 4
 | 50 | 48.592 | 48.495 | 8.944 | 7.172 | 4.326 | 4.177 | 4
Hylam | 110 | 104.91 | 104.72 | 21.364 | 15.142 | 5.154 | 4.6241 | 4
 | 50 | 47.793 | 47.707 | 11.535 | 8.835 | 4.496 | 4.27 | 4

## Slide 4: Pipeline Model and Inputs
Layer | Thickness | k (W/m·K) | Purpose
Steel pipe (ID 400 mm) | 20 mm | 45 | Carries the oil and withstands internal pressure
Thermal insulation | 50 mm | 0.025 to 0.25 | Main barrier: limits heat loss to keep oil above 45 °C
Polymer jacket | 5 mm | 0.30 | Necessary to keep seawater out of the insulation (wet insulation conducts far more heat) and to guard against abrasion and impact
Concrete coating | 50 mm | 1.7 | Necessary to add submerged weight so the pipe stays on the seabed against currents, and to protect against impact
Biofouling | 1 mm | 0.6 | Marine growth on the outer surface, modelled as a thin film
10 km
pipe length
106.8 kg/s
oil mass flow
2200 J/kg·K
oil specific heat
100 / 500
h oil / sea, W/m²·K
4 °C
seawater
45 °C
wax threshold
110 / 50 °C
oil inlet

## Slide 5: Formulae Used
Total resistance per metre, R′ (K·m/W)
Oil temperature along the pipe
Heat loss per metre at distance x
Waxing distance, 110 °C inlet (oil reaches 45 °C)
Waxing distance, 50 °C inlet (oil reaches 45 °C)
r: radius, k: conductivity, h: film coefficient, ṁ: mass flow, C_p: specific heat, T∞ = 4 °C. 106/41 = (110 − 4)/(45 − 4) and 46/41 = (50 − 4)/(45 − 4).

## Slide 6: Results: Heat Loss and Temperature, 110 °C Inlet
Insulation | k (W/m·K) | R′ (K·m/W) | Heat loss (W/m) | T at 10 km (°C) | Wax dist. (km)
Aerogel | 0.025 | 1.339 | 79.5 | 106.68 | 299.0
Rigid PU Foam | 0.03 | 1.122 | 94.5 | 106.05 | 250.5
Adv. Syntactic Foam | 0.12 | 0.307 | 345.2 | 96.28 | 68.6
Syntactic PP | 0.15 | 0.253 | 419.4 | 93.58 | 56.4
Wood | 0.15 | 0.253 | 419.4 | 93.58 | 56.4
Solid PP | 0.2 | 0.198 | 534.2 | 89.54 | 44.3
Hylam | 0.25 | 0.166 | 639.2 | 86.01 | 37.0
Every insulation keeps the oil above 45 °C, but Aerogel and Rigid PU Foam lose by far the least heat (79.5 and 94.5 W/m).
Green: oil stays at or above 45 °C (no waxing). Red: oil falls below 45 °C (waxing risk).

## Slide 7: Results: Heat Loss and Temperature, 50 °C Inlet
Insulation | k (W/m·K) | R′ (K·m/W) | Heat loss (W/m) | T at 10 km (°C) | Wax dist. (km)
Aerogel | 0.025 | 1.339 | 34.3 | 48.56 | 36.2
Rigid PU Foam | 0.03 | 1.122 | 41.0 | 48.29 | 30.3
Adv. Syntactic Foam | 0.12 | 0.307 | 149.8 | 44.05 | 8.3
Syntactic PP | 0.15 | 0.253 | 182.0 | 42.87 | 6.8
Wood | 0.15 | 0.253 | 182.0 | 42.87 | 6.8
Solid PP | 0.2 | 0.198 | 231.8 | 41.12 | 5.4
Hylam | 0.25 | 0.166 | 277.8 | 39.59 | 4.5
Only Aerogel (48.6 °C) and Rigid PU Foam (48.3 °C) keep the oil above 45 °C; every other option falls into the waxing region.
Green: oil stays at or above 45 °C (no waxing). Red: oil falls below 45 °C (waxing risk).

## Slide 8: Visualization: Oil Temperature after 10 km
Chart: Temperature (°C)
| Aerogel | Rigid PU | Adv. Syntactic | Syntactic PP | Wood | Solid PP | Hylam
110 °C inlet | 106.68 | 106.05 | 96.28 | 93.58 | 93.58 | 89.54 | 86.01
50 °C inlet | 48.56 | 48.29 | 44.05 | 42.87 | 42.87 | 41.12 | 39.59
Wax threshold (45 °C) | 45 | 45 | 45 | 45 | 45 | 45 | 45
At 110 °C all options pass; at 50 °C only Aerogel and Rigid PU Foam stay above the 45 °C threshold.

## Slide 9: Visualization: ANSYS Thermal Simulation
ANSYS 2023 R1 steady-state thermal model with oil-side and seawater-side convection. The radial temperature drop is concentrated across the insulation layer.
Simulation for Aerogel

## Slide 10: Visualization: ANSYS Thermal Simulation
ANSYS 2023 R1 steady-state thermal model with oil-side and seawater-side convection. The radial temperature drop is concentrated across the insulation layer.
Simulation for Rigid PU Foam

## Slide 11: Critical Radius of Insulation
For a cylinder with outer convection
rcr = k / ho
If the outer radius r_o is above r_cr, adding insulation always reduces heat loss, because conduction resistance dominates.
Insulation outer radius = 270 mm, far above every r_cr (under 0.5 mm)
Insulation | k (W/m·K) | r_cr (mm)
Aerogel | 0.025 | 0.05
Rigid PU Foam | 0.03 | 0.06
Adv. Syntactic Foam | 0.12 | 0.24
Syntactic PP | 0.15 | 0.30
Wood | 0.15 | 0.30
Solid PP | 0.2 | 0.40
Hylam | 0.25 | 0.50
Evaluated with seawater-side h_o = 500 W/m²·K

## Slide 12: Industrial Decision
Decision: specify Aerogel or Rigid PU Foam. They cut heat loss 4 to 8 times and are the only options that keep 50 °C oil above 45 °C after 10 km.
Aerogel
Lowest heat loss (79.5 W/m at 110 °C). Use in pipe-in-pipe or hydrophobic packs, since it loses performance when wet.
Rigid PU Foam
Near-aerogel performance (94.5 W/m). It crushes under deep-sea pressure: use in shallow water with a jacket, or syntactic PU in deep water.
All other options
Syntactic PP and foam, solid PP, wood and Hylam pass at 110 °C but fall to 39.6 to 44.0 °C at 50 °C. They need thicker layers or hotter oil.
Problems Faced

## Slide 13: Solution
If PU foam is crushed
Switch to syntactic PU (glass microspheres) in deep water
Add a pressure-rated outer jacket or pipe-in-pipe
Use denser foam and prove it by pressure testing
If aerogel gets wet
Use hydrophobic aerogel in sealed, vacuum-packed layers
Keep it in a dry, gas-filled pipe-in-pipe annulus
Seal field joints and allow a wet-conductivity margin
What “thermal stress” means
It is the strain from running hot caused due to uneven expansion across the wall and softening at high temperature.
At 110 °C PU Foam is workable with very little margin as it is rated to about 100 to 130 °C.
Aerogel packs are rated to about 200 °C providing ample margin.